## Slide 1: Time Series Super Powers
Understanding the Fourier Transform, FFT, and Basic Time-series Analysis

## Slide 2: This is the story of a moving point
This type of motion, moving to the right, slowing to a start and then moving to the left - has a name. It's called "sinusoidal" motion.
position = cos(time)

## Slide 3: Then it moved in 2 dimensions
This points motion in both dimensions was independent of each other. For various reasons we call the two dimensions this point moves in the *real* and the *imaginary* axis. In fact though, there's nothing truly imaginary about it.
Horizontal Dimension
“real”
Vertical Dimension
“Imaginary”
Horizontal Position = cos(time)
Vertical
Position = sin(time)

## Slide 4: Sine + Cosine is A Circle
Horizontal Dimension = sin(time)
Vertical Dimension = cos(time)
REPLACE WITH IMAGE
Notes: Point rotating around a circle.

## Slide 5: A Pointing Rotating Around A Circle
1 revolution is a circumference
1 circumference is 2π radiuses
In 1 second the point travels 2π radius.
Notes: Speed is frequency. The number of revolutions per second.

## Slide 6: Points Rotate At Different Speeds
Think of hands of a clock. The hands move at different speeds/frequencies.
Hour hand - 2π radius/3600 seconds
Minute hand - 2π radius/60 seconds
Second hand - 2π radius/1 second
2π2.77e-4 Hz
2π1.66e-2 Hz
2π1 Hz
Notes: Circles rotating at different speeds.

## Slide 7: Time Series of Measured Data
Digital data is discrete and measured at a fixed interval.
Time time axis is really samples.
Samples are collected every Ts seconds, or a frequency of Fs = 1/Ts
Notes: Examples of measured data?

## Slide 8: Projecting Onto the Circle
Notes: The value of the measured data controls the LENGTH of the “arm” of the clock face. The frequency determines the angle in 2 dimensions.

## Slide 9: What if we Wrapped Our Signal Around a Circle?
1 dimensional data becomes 2 dimensional data!
Notes: The green “line” represents many individual points mapped around the circle. There are hundreds of points.
The “time” dimension has been trasferred to a “spatial” dimension – time determines how far around the circle the points map.

## Slide 10: What Happened to Time?
Time is been transferred to the position of the “clock hand” around the circle.
Time passes – Ts
Distance passes – speed x time
Distance:
(2πf Ts) radius/seconds x seconds
2Ts
3Ts

## Slide 11: Mapping the Signal on Different Frequency Circles
As frequency of the circle goes up, the signal gets stretched further around the circle. At each time step (Ts) of the measured signal the “clock hand” travels around the circle.

## Slide 12: So Now we Have a Bunch of Measurements in 2 Dimensions …
Each measured point now lives in 2 dimensions.
We call this a “vector”.
We can add vectors together.
Let’s SUM ALL THE POINTS.

## Slide 13: Adding 2Dimensional Lines
These are called “vectors” – add dimensions independently.
A
B
A+B = C
A
B
Points on opposite sides add destructively – get smaller.
Points “near” each other add together to be bigger.

## Slide 14: Vectors have Lengths and Angles
A point in 2 dimensions can be expressed by it’s horizontal and vertical location OR
Described by it’s length and angle.
Length
Angle
Point

## Slide 16: Average the 2D Signal
Average all the 2D points
Find the length of the average vector

## Slide 17: How about a different Signal?

## Slide 18: How about a Different Signal?

## Slide 19: Leonard Euler
We can write the sum of a cosine and and sine in two dimensions in a compact form:
Notes: Attribution: http://www-history.mcs.st-andrews.ac.uk/Biographies/Euler.html

## Slide 20: Mathematically This Is
x[n]
n: 1 2 3 … N
exp(-j2πf1)
exp(-j2πf2)
exp(-j2πf3)
X[fk] = SUMn(x[n] * exp[-j2πfk* {n/N} ] )
n/N – the percentage of distance around the circle for each sample.
Notes: Discrete Fourier Transform!

## Slide 21: The Process
Pick Frequency K
Arrange Measured Points around Circle of Frequency K
Average All Points
Compute Length and Angle of Average Vector
Measure Data
Plot Power vs. Frequency
FFT

## Slide 22: Dot Product of Measurements and Phase Vector
Time Series
Phase Vectors
X
Σ

## Slide 23: Take Note
The sample rate (Ts) doesn’t explicitly appear in the equation. It’s independent of the math and is used for interpretation.
There’s no point in measuring frequencies greater than (Sampling Frequency)/2.
Each frequency fk is computed by taking the sum of ALL MEASURED POINTS.

## Slide 24: A View in Reverse
You can also think of a measured signal as being approximated by the sum of many rotating circles:
Notes: http://en.wikipedia.org/wiki/Fourier_series

## Slide 25: Python!
ft = []
for frequency in frequences:
average_point = 0. + 1*j*0.
for n,meas in zip(range(1,N_measurements),measurements):
fractional_distance = float(n)/N_measurements
average_point += meas*np.exp(-1j*2*pi*frequency*fractional_distance)
average_point /= average_point / N_measurements
ft.append(average_point)
Ft is a vector of complex numbers – the real and imaginary location of each point. The length is abs(ft)

## Slide 26: Fast Fourier Transform (FFT)
The naive discrete Fourier transform is O(N2)
Cooley-Tukey reduced to O(n log n) – the Fast Fourier Transform (FFT).
J. Cooley
J. Tukey

## Slide 27: What Does the FFT Return?
FFT(x,N):
X – time series
N – number of bins to calculate
The transform is symmetric around Fs/2:
e.g. If you sample at 100 Hz, the FFT(10Hz) will look like FFT(190 Hz).
The function returns the FFT evaluated from 0 Hz all the way up to Fs Hz – half of this is redundant*.
*If your measured signal is complex, this isn’t true. This is rarely the case.
x[n]
FFT[k]
k is from 0 to N
You only care about FFT[0] to FFT[N/2]. Usually you only care about the absolute value of the complex (2 dimensional) output.

## Slide 28: What Frequencies Does the Output Correspond to?
N_fft = 256.0
Fs = 200
freqsig = fft.fft(sig,n=N_fft)
sig
abs(freqsig)
freq_axis = np.arange(0,Fs,Fs/N_fft)

## Slide 29: How Many Bins?
Each array element of the FFT corresponds to a frequency bin. Each bin is Fs/N_FFT wide.
The more measurements you have, the better precision you get (limited by floor(log2(N_samples))
FFT

## Slide 30: Practical Note: Windowing Functions
Animate signal with and without window function –

## Slide 31: Show FFT with varying number of Bins

## Slide 32: Helpful Resources
http://www.dspguide.com/ch8/6.htm